## Slide 1: General purpose PLL 2026 May 27
Super Long Wave Yutaka Kotani (team leader) yutaka.kotani.in@gmail.com Ashutosh Chakravarty Cheng Fei

## Slide 2: Agenda
1
Project information
2
Team background
3
Specification
4
Block diagram
5
Circuit design
6
Layout
7
Evaluation
8
Schedule

## Slide 3: Project information
Goal
  Creating general purpose PLL
  Creating a part of FM Radio component
Design
  PLL has two mode
  Clock multiplier mode
  FM demodulator mode
Application
  Digital clock generator & FM Radio
Reference
  TI CD4046B Application Report SCHA002A
AMP & Speaker
PD
PLL
VCO
FMTuner & LNA
Charge pump
65-80MHz
Audio Signal
Loop Filter
LPF
Buffer
Clock multiplier mode
CPU
PFD
PLL
VCO
Crystal Oscillator
Charge pump
Loop Filter
Divider
CLK:80MHz
Buffer
2x Current Source
Center Frequency & KVCO adjust
CLK:10MHz
Center Frequency & KVCO adjust
FM demodulator mode
2x Current Source

## Slide 4: Team background
 | Yutaka Kotani | Ashutosh Chakravarty | Cheng Fei
Discode name | Yutaka KOTANI | Teddy | buttercutter
Academic experience | Bachelor of Computer Science | EE | Bachelors in EE
Work experience | Field Application engineer in Semiconductor company | Digital Design Engineer | Analog Design Engineer with tape out experience

## Slide 5: Specification
Target Spec | Min | Typ | Max
Pin count | 11 |  | 
Estimated Area | 999um2 |  | 
Vdd voltage [V] | 3 | 3.3 | 3.6
pll_in voltage [V] | 0.8 | - | 2.5
pll_out voltage [V] | 0 |  | vdd
Pin | Pin name | Notes
1 | VDD | 3.3V
2 | GND | 
3 | PLL_IN | Reference clk input
4 | PLL_OUT | Clock multiplier output
5 | CEN_FREQ_CUR | Center frequency bias current
6 | KVCO_ADJ_CUR | kvco adjust bias current
7 | MODE_SEL | Hi: Use FM demodulator Low: Use Clock multiplier
8 | EXT_FIL_OUT | To Band pass filter 10.7MHz
9 | EXT_FIL_IN | From Band pass filter 10.7MHz
10 | LF_IN | External Loop filter input
11 | LF_OUT | External Loop filter output
Clock multiplier mode | Min | Typ | Max
pll_in frequency [MHz] | 9.9 | 10 | 10.1
pll_out frequency [MHz] | 79.9 | 80 | 80.1
Divider ratio |  | 1/8 | 
Cen_freq_cur [uA] | 90 | 100 | 110
FM demodulator mode | Min | Typ | Max
pll_in frequency [MHz] | 76 | - | 90
dmod_out voltage [V] | 0 | - | vdd
Cen_freq_cur [uA] | 10 | - | 110

## Slide 6: Block diagram - Clock multiplier mode
VCO
-
+
φin
1 π
Duty -1 to 1
Ibias
Kvco
1/N
PFD
Charge
pump
φdiv
R1
Divider
Current
-Ibias to Ibias
Voltage
Vin
Phase
REF CLK
∫
1 C1
+
∫
φout
OUT CLK
φout
Phase
Phase
Transfer function: Ibias Kvco
G(s) = ------- * (R1+1/C1s) * ------- π s H(s) = 1 / N
Closed loop: G(s) W(s) = ---------------------- 1 + G(s) H(s) Open loop: G(s) H(s)
+
CEN_FREQ_CUR
Center Frequency
Current
KVCO_ADJ_CUR
External Loop filter
lf_out
lf_in
Adjust KVCO

## Slide 7: Block diagram – FM demodulator mode
VCO
-
+
φin
1 π
Duty -1 to 1
Ibias
Kvco
PD
Charge
pump
R1
Current
-Ibias to Ibias
Voltage
Vin
Phase
FM in
∫
1 C1
+
∫
lf_out
FM Demodulator out
External Loop filter
Phase
+
Current
lf_in
CEN_FREQ_CUR
Center Frequency
KVCO_ADJ_CUR
Adjust KVCO

## Slide 8: Circuit design - VCO

## Slide 9: Circuit design – PFD

## Slide 10: Circuit design - OPAMP

## Slide 11: Circuit design – Beta multiplier reference

## Slide 12: Layout (T.B.D)

## Slide 13: Evaluation (T.B.D)
Put evaluation result here
Insert graph to left

## Slide 14: Schedule
Week | Date | Event | Track Details
Week 23 | June 5 | Team Formation Deadline | 
Week 24 | June 12 | Project Proposal Review | 
Week 27 | July 3 | Schematic Review | 
Week 28 | July 10 | Simulation Review (blocks) | 
Week 29 | July 17 | Simulation Review (top level) | 
 |  | READiness Check & Go/No-go Decision | 
Week 33 | Aug 14 | Layout Review (blocks) | 
Week 34 | Aug 21 | Layout Review (top level) | 
Week 35 | Aug. 28 | Verification | 
 |  | Final Chip Review | 
 |  | Final Submission | 
 |  | Upload of Chip Test Results |