## Slide 1: General purpose PLL
Team X Yutaka KOTANI Jay Teddy Butter cutter

## Slide 2: Agenda
1
Project overview
2
Block diagram
3
Specification
4
Circuit design
5
Evaluation
6
Layout
7
PEX & Validation
8
Schedule

## Slide 3: Project overview
Team member and role
  Yutaka KOTANI – Team leader, VCO
  Jay - PFD
  Teddy - Divider
  Butter cutter - PFD
PLL for general purpose
  High speed CPU clock generation
  FM radio demodulator
PLL has two mode
  Clock multiplier mode
  FM demodulator mode
AMP & Speaker
PD
PLL
VCO
FMTuner & LNA
Charge pump
Loop Filter
65-80MHz
Audio Signal
10.7MHzBPF
External LPF
Buffer
Current Source
Center Frequency
Clock multiplier mode
CPU
PFD
PLL
VCO
Crystal Oscillator
Charge pump
Loop Filter
Divider
80MHz
Buffer
Current Source
Center Frequency
10MHz
FM demodulator mode

## Slide 4: Block diagram - Clock multiplier mode
VCO
-
+
φin
1 π
Duty -1 to 1
Ibias
Kvco
1/N
PFD
Charge
pump
φdiv
R1
Divider
Current
-Ibias to Ibias
Voltage
Vin
Phase
REF CLK
∫
1 C1
+
∫
φout
OUT CLK
Loop filter
φout
Phase
Phase
Transfer function: Ibias Kvco
G(s) = ------- * (R1+1/C1s) * ------- π s H(s) = 1 / N
Closed loop: G(s) W(s) = ---------------------- 1 + G(s) H(s) Open loop: G(s) H(s)
+
CEN_FREQ_CUR
Center Frequency
Current

## Slide 5: Block diagram – FM demodulator mode
VCO
-
+
φin
1 π
Duty -1 to 1
Ibias
Kvco
PD
Charge
pump
R1
External 10.7MHzBPF
Current
-Ibias to Ibias
Voltage
Vin
Phase
FM in
∫
1 C1
+
∫
vout
FM Demodulator out
Loop filter
Phase
+
CEN_FREQ_CUR
Center Frequency
Current
BPF

## Slide 6: Specification (T.B.D)
Target Spec | Min | Typ | Max
Pin count | 9 |  | 
Estimated Area | 999um2 |  | 
Vdd voltage [V] | 3 | 3.3 | 3.6
pll_in voltage [V] | 0.8 | - | 2.5
pll_out voltage [V] | 0 |  | vdd
Pin | Pin name | Notes
1 | VDD | 3.3V
2 | GND | 
3 | PLL_IN | Reference clk input
4 | PLL_OUT | Clock multiplier output
5 | CEN_FREQ_CUR | Center frequency bias current
6 | MODE_SEL | Hi: Use FM demodulator Low: Use Clock multiplier
7 | EXT_FIL_OUT | To Band pass filter 10.7MHz
8 | EXT_FIL_IN | From Band pass filter 10.7MHz
9 | DMOD_OUT | FM demodulator output
Clock multiplier mode | Min | Typ | Max
pll_in frequency [MHz] | 9.9 | 10 | 10.1
pll_out frequency [MHz] | 79.9 | 80 | 80.1
Divider ratio |  | 1/8 | 
Cen_freq_cur [uA] | 90 | 100 | 110
FM demodulator mode | Min | Typ | Max
pll_in frequency [MHz] | 76 | - | 90
dmod_out voltage [V] | 0 | - | vdd
Cen_freq_cur [uA] | 10 | - | 110

## Slide 7: Circuit design - VCO

## Slide 8: Circuit design – module name

## Slide 9: Evaluation (T.B.D)
Put evaluation result here
Insert graph to left

## Slide 10: Layout (T.B.D)

## Slide 11: PEX & Validation (T.B.D)

## Slide 12: Schedule
Week | Date | Event | Track Details
Week 23 | June 5 | Team Formation Deadline | 
Week 24 | June 12 | Project Proposal Review | 
Week 27 | July 3 | Schematic Review | 
Week 28 | July 10 | Simulation Review (blocks) | 
Week 29 | July 17 | Simulation Review (top level) | 
 |  | READiness Check & Go/No-go Decision | 
Week 33 | Aug 14 | Layout Review (blocks) | 
Week 34 | Aug 21 | Layout Review (top level) | 
Week 35 | Aug. 28 | Verification | 
 |  | Final Chip Review | 
 |  | Final Submission | 
 |  | Upload of Chip Test Results |