## Slide 1: General purpose PLL 2026 July 4
Super Long Wave Yutaka Kotani (team leader) yutaka.kotani.in@gmail.com Ashutosh Chakravarty Cheng Fei Fatima

## Slide 2: Agenda
1
Project information
2
Design objective
3
System overview
4
Schematic summary
6
Verification status
7
Design checklist
8
Open issues
9
Questions for reviewers
5
Design assumptions

## Slide 3: Design objective
What problems circuit solves
  The PLL extracts the audio signal by performing FM demodulation on the 10.7 MHz intermediate frequency (IF) signal from the preceding radio front-end.
Target specifications
  Input FM modulated IF 10.7MHz
  Output FM demodulated audio signal
Intended Use
  Create FM radio demodulator
Project scope and spec changes Following our mentor's advice, we have reduced the project scope and specifications.
  Clock multiplier mode was deleted
  Input signal was changed from a direct FM signal to an intermediate frequency of 10.7 MHz
AMP & Speaker
PFD
PLL
VCO
FM radio Frontend
Charge pump
10.7MHz
Audio Signal
Loop Filter
LPF
Buffer
Clock multiplier mode
CPU
PFD
PLL
VCO
Crystal Oscillator
Charge pump
Loop Filter
Divider
CLK:80MHz
Buffer
2x Current Source
Center Frequency & KVCO adjust
CLK:10MHz
Center Frequency adjust
FM demodulator mode
Current Source
*1
*2

## Slide 4: System overview
PFD * buttercutter write here.
Charge pump * fa_84 write here.
Loop filter (external) * fa_84 write here.
Buffer * Teddy write here.
LPF (external) * Teddy write here.
VCO * Yutaka KOTANI write here.
Current source (external) * Yutaka KOTANI write here.
AMP & Speaker
PFD
PLL
VCO
FM radio Frontend
Charge pump
10.7MHz
Audio Signal
Loop Filter
LPF
Buffer
Mosbius chip internal
Current Source
Up to 15KHz

## Slide 5: Specification
Target Spec | Min | Typ | Max
Pin count | 9 |  | 
Estimated Area | ***um2 |  | 
Vdd voltage [V] | 3 | 3.3 | 3.6
pll_in voltage [V] | 0.8 | - | 2.5
pll_out voltage [V] | 0 |  | vdd
Pin | Pin name | Notes
1 | VDD | 3.3V
2 | GND | 
3 | PLL_IN | Reference clk input
4 | PLL_OUT | Clock multiplier output
5 | CEN_FREQ_CUR | Center frequency bias current
6 | KVCO_ADJ_CUR | kvco adjust bias current
7 | MODE_SEL | Hi: Use FM demodulator Low: Use Clock multiplier
8 | LF_IN | External Loop filter input
9 | LF_OUT | External Loop filter output
Clock multiplier mode | Min | Typ | Max
pll_in frequency [MHz] | 9.9 | 10 | 10.1
pll_out frequency [MHz] | 79.9 | 80 | 80.1
Divider ratio |  | 1/8 | 
Cen_freq_cur [uA] | 90 | 100 | 110
FM demodulator mode | Min | Typ | Max
pll_in frequency [MHz] | 76 | - | 90
dmod_out voltage [V] | 0 | - | vdd
Cen_freq_cur [uA] | 10 | - | 110

## Slide 6: Block diagram - Clock multiplier mode
VCO
-
+
φin
1 π
Duty -1 to 1
Ibias
Kvco
1/N
PFD
Charge
pump
φdiv
R1
Divider
Current
-Ibias to Ibias
Voltage
Vin
Phase
REF CLK
∫
1 C1
+
∫
φout
OUT CLK
φout
Phase
Phase
Transfer function: Ibias Kvco
G(s) = ------- * (R1+1/C1s) * ------- π s H(s) = 1 / N
Closed loop: G(s) W(s) = ---------------------- 1 + G(s) H(s) Open loop: G(s) H(s)
+
CEN_FREQ_CUR
Center Frequency
Current
KVCO_ADJ_CUR
External Loop filter
lf_out
lf_in
Adjust KVCO

## Slide 7: Schematic summary - PFD
Put your schematic diagram here
Purpose
Input and Output
  Input
  output
Important design decisions
Interface to other blocks

## Slide 8: Schematic summary – Charge pump
Put your schematic diagram here
Purpose
Input and Output
  Input
  output
Important design decisions
Interface to other blocks

## Slide 9: Schematic summary – Loop filter
Put your schematic diagram here
Purpose
Input and Output
  Input
  output
Important design decisions
Interface to other blocks

## Slide 10: Schematic summary – Buffer
Schematic (Buffer, Inverter respectively)
Purpose
To copy the voltage from the loop filter to the VCO. This ensures a reliable input
Input and Output
  Input 3V pulse signal (for simulation)
  Output 3V pulse signal identical to input (simulation result)
  3V VDD input

## Slide 11: Simulations of Buffer
Output of the Buffer
Output Of Inverter

## Slide 12: Schematic summary – LPF
Schematic
Purpose For removing high frequency components from buffer for smoother output
Input and Output
  Buffered signal containing high frequency and noise
  Clean filtered signal
Important design decisions: Selection of R and C values of reasonable size for filter design
Interface to other blocks Input from buffer

## Slide 13: Resistor and Capacitor Value Selection
Resistor Selection
Capacitor Selection

## Slide 14: Simulation of LPF

## Slide 15: Schematic summary – VCO
Put your schematic diagram here
Purpose
Input and Output
  Input
  output
Important design decisions
Interface to other blocks

## Slide 16: Schematic summary – current source
Put your schematic diagram here
Purpose
Input and Output
  Input
  output
Important design decisions
Interface to other blocks

## Slide 17: Circuit design - VCO

## Slide 18: Circuit design – PFD

## Slide 19: Circuit design - OPAMP

## Slide 20: Circuit design – Beta multiplier reference

## Slide 21: Layout (T.B.D)

## Slide 22: Evaluation - VCO
to left
y = 9.04099539e+15 * x^2-4.55009586e +11 * x + 2.24254037e+07

## Slide 23: Evaluation - OPAMP
to left

## Slide 24: Application block diagram – FM radio
VCO
-
+
φin
1 π
Duty -1 to 1
Ibias
Kvco
PD
Charge
pump
R1
Current
-Ibias to Ibias
Voltage
Vin
Phase
Antena in
∫
1 C1
+
lf_out
FM Demodulator out
External Loop filter
Phase
+
Current
lf_in
CEN_FREQ_CUR
Center Frequency
KVCO_ADJ_CUR
Adjust KVCO
BPF

## Slide 25: Schedule
Week | Date | Event | Track Details
Week 23 | June 5 | Team Formation Deadline | 
Week 24 | June 12 | Project Proposal Review | 
Week 27 | July 3 | Schematic Review | 
Week 28 | July 10 | Simulation Review (blocks) | 
Week 29 | July 17 | Simulation Review (top level) | 
 |  | READiness Check & Go/No-go Decision | 
Week 33 | Aug 14 | Layout Review (blocks) | 
Week 34 | Aug 21 | Layout Review (top level) | 
Week 35 | Aug. 28 | Verification | 
 |  | Final Chip Review | 
 |  | Final Submission | 
 |  | Upload of Chip Test Results |